CompactFlash

乙太網路介面卡

For Windows CE-based PDA / Palm PCs/Pocket PCs

使用手冊

# FCC REGULATORY STATEMENTS

Part15, Class B

This device complies with Part 15 of FCC rules. Operation is subject to the following two conditions:

- This device may not cause harmful interface, and

- This device must accept any interface received, including interface that may cause undesired operation. This equipment has been tested and found to comply with the limits for a Class B digital device, pursuant to Part 15 of the FCC Rules. These limits are designed to provide reasonable protection against harmful interference in a residential installation. This equipment generates, uses and can radiate radio frequency energy, and if not installed and used in accordance with the instructions, may cause harmful interference to radio communications. However, there is no guarantee that interference will not occur in a particular installation. If this equipment does cause harmful interference to radio or television reception, which can be determined by turning off and on, the user is encouraged to try to correct the interference by one or more of the following measures:

- Reorient or relocate the receiving antenna.

- Increase the distance between the equipment and receiver.

- Connect the equipment into an outlet on a circuit different from that to which the receiver is connected.

Changes or modifications not expressly approved by party responsible for compliance could  void the user the user authority to operate the equipment.

CF乙太網路卡

適用於Windows CE作業系統的個人數位助理器（PDA)。

功能簡介

- 符合CF+/CompactFlash 1.4版規格

- 可使用於配備有CompactFlash插槽的WinCE個人數位助理或掌上型電腦上

- 提供簡易安裝程式

- 耗電率低且無須外接電源

- 提供偵錯LED指示燈, 可顯示Link及Activity等訊息

產品規格

網路介面

- 符合IEEE 802.3 10BaseT乙太網路規格

- 與NE2000相容

- 提供10 Mbps資料傳輸速度

作業系統

- Windows CE 2.0 or newer that supports synchronization from Microsoft Windows 95/98 and Windows NT.4.0.

電力需求

- 正常操作狀態: +3.3V, 50mA max

實體規格

- Type I CompactFlash I/O 介面

- 體積88mm x 42.8mm x 3.3mm

- 重量30gw

LED 指示燈

- Link (橘色:表正常連線)

- Act (綠色閃爍:表資料傳送中)

EMI 及 PTT 安規

- FCC part 15 Class B

- CE Mark EN55002 Class B, EN50081-2

- VCCI Class BThis CompactFlash Size Ethernet LAN Card is designed for Windows CE-based palm-sized PCs, pocket PC, handheld PCs and any computer with a CompactFlash slot.

外部環境需求

- 操作溫度：32(F to 149(F   (0(C to 65(C)

- 儲存溫度：-4(F to 158(F   (0(C to 70(C)

- 溼度：	10% - 90% , noncondensing

## 細部零件說明

# 硬體安裝說明

以下說明將以「CF網路卡」來簡稱「CompactFlash 乙太網路卡」。

## 插入CF卡

如下圖所示將CF網路卡插入PDA的Compact Flash插槽

## 連接至網路

在載入網路驅動程式之前，先將UTP網路線一端的RJ-45連接頭，連接至CF網路卡的網路連接埠

# Windows CE 2.0/2.11/3.0 軟體設定

- 將您的Windows CE based PDA/Palm PC 與 Host PC連接，一般Host PC 使用的作業系統為 Windows9x/NT

- 從WinCE Services CD中安裝“ActiveSync”至您的 desktop PC中；詳細安裝說明請參閱 Online help.

- 將PDA/Palm PC連接至 Host PC的 COM1 或 COM2連接埠

- 連接完成之後在Host PC上的“My Computer”資料夾中會出現“Mobile device” 的圖示

- 將本產品所附的驅動程式磁碟片放入磁碟機中，並打開“Windows Explorer”執行A磁碟中的“setup.exe”程式

- 將CF網路卡插入CF插槽中，然後將PDA/Palm PC重新開機

- 雙擊 “Network”圖示，選取“property” 後再選取 “Obtain an IP address through DHCP sever”。這時，您將可以看到“CompactFlash Size Ethernet LAN Card” 已安裝完成並出現在 WinCE畫面中

- 如果您的網路上沒有DHCP伺服器，那麼您就必須自行在“Specific an IP address”選項中去設定IP位址

Note: Host PC's執行Windows 95 OSR2 如果在suspend模式時，則不能啟動序列埠(sync)。請重新開機以便啟動序列埠(sync)。.