# Compact Flash

# 10/100 高速乙太網路介面卡

For Both Notebook PC and

Windows CE-based PDA / Palm PC

使用手冊

# FCC REGULATORY STATEMENTS

Part15, Class B

This device complies with Part 15 of FCC rules. Operation is subject to the following two conditions:

- This device may not cause harmful interface, and

- This device must accept any interface received, including interface that may cause undesired operation. This equipment has been tested and found to comply with the limits for a Class B digital device, pursuant to Part 15 of the FCC Rules. These limits are designed to provide reasonable protection against harmful interference in a residential installation. This equipment generates, uses and can radiate radio frequency energy, and if not installed and used in accordance with the instructions, may cause harmful interference to radio communications. However, there is no guarantee that interference will not occur in a particular installation. If this equipment does cause harmful interference to radio or television reception, which can be determined by turning off and on, the user is encouraged to try to correct the interference by one or more of the following measures:

- Reorient or relocate the receiving antenna.

- Increase the distance between the equipment and receiver.

- Connect the equipment into an outlet on a circuit different from that to which the receiver is connected.

( Changes or modifications not expressly approved by party responsible for compliance could void the user the user authority to operate the equipment.

# 簡介

本產品「CompactFlash高速乙太網路介面卡」，以下簡稱「CF網路卡」，可使用在Windows CE-based 掌上型 PCs、個人數位助理PDA等配備有CompactFlash 插槽的機器上。

另外，還可藉由PCMCIA轉接卡，將CF網路卡使用在配備有PCMCIA插槽的筆記型電腦上，一卡可以兩用。

CF網路卡在安裝及使用上均非常簡便，且無須外接任何電源，是您的PDA上網非常重要的一個周邊設備。

## 系統需求

### 使用在Notebook PC:

- 與IBM 相容且配備有386SX等級以上的中央處理器

- 至少一個 Type II PC Card 插槽

- 已安裝PCMCIA release 2.1 compliant Card Services及 Socket Services.

### 使用在Windows CE-based PDA/Palm PC:

- 一個 Type I CompactFlash 插槽並支援 IO functionality.

- 作業系統為Windows CE 2.0  或更新版本

- Windows CE Service 磁碟片

- 已安裝CF+ and CompactFlash Spec. Reversion 1.4   compliant Card Services and Socket Services

## 支援的作業系統

### For Notebook PC:

Novell Netware 3.x/4.x

Microsoft LAN Manager

Packet Driver Applications

Microsoft Windows for Workgroups 3.11

Microsoft Windows 3.1

Microsoft Windows NT 3.51, NT 4.0

Windows 95

Windows 98

Windows 2000

Lantastic 6.0

IBM OS/2 Warp Version 3

### For Windows CE-based PDA/Palm PC:

軟體相容

Windows CE 2.0 or newer version

硬體中央處理器相容

Supports PDA/Palm PC using MIPS4000 series, and Hitachi Sh3 series processors.

## 細部零件說明

# 硬體安裝

## 連接至 PDA/Palm PC

如下圖將 CF網路卡 插入CompactFlash插槽中

## 連接至 Notebook PC

- 將 CF網路卡平行插入轉接卡中，即可轉換成標準的PCMCIA type II PC卡

- 如下圖所示將轉接卡插入電腦中的PCMCIA插槽

## 連接至網路

在載入網路驅動程式之前，先將UTP網路線一端的RJ-45連接頭，連接至CF網路卡的網路連接埠

# 軟體安裝（For PDA/Palm PC with Windows CE 2.0）

- 將您的Windows CE based PDA/Palm PC 與 Host PC連接，一般Host PC 使用的作業系統為 Windows9x/NT

- 從WinCE Services CD中安裝“ActiveSync”至您的 desktop PC中；詳細安裝說明請參閱 Online help.

- 將PDA/Palm PC連接至 Host PC的 COM1 或 COM2連接埠

- 連接完成之後在Host PC上的“My Computer”資料夾中會出現“Mobile device” 的圖示

- 將本產品所附的驅動程式磁碟片放入磁碟機中，並打開“Windows Explorer”執行A磁碟中的“setup.exe”程式

- 將CF網路卡插入CF插槽中，然後將PDA/Palm PC重新開機

- 雙擊 “Network”圖示，選取“property” 後再選取 “Obtain an IP address through DHCP sever”。這時，您將可以看到“CompactFlash Size 10/100 Fast Ethernet LAN Card ” 已安裝完成並出現在 WinCE畫面中

- 如果您的網路上沒有DHCP伺服器，那麼您就必須自行在“Specific an IP address”選項中去設定IP位址

Note: Host PC's執行Windows 95 OSR2 如果在suspend模式時，則不能啟動序列埠(sync)。請重新開機以便啟動序列埠(sync)。.

# Appendix A.	產品規格

網路介面

- 符合IEEE 802.3 10BaseT乙太網路規格

- 符合IEEE 802.3u 100BaseT高速乙太網路規格

- 提供10 Mbps或100Mbps資料傳輸速度

作業系統

- Novell Netware 3.x, 4.x

- Microsoft LAN Manager

- Packet Driver Applications

- Microsoft Windows for Workgroups 3.11

- Windows 3.1

- Microsoft Windows NT 3.51, NT 4.0

- Windows 95

- Windows 98

- Windows 2000

- Windows CE 2.0 or newer

- Lantastic 6.0

- IBM OS/2 Warp Version 3

連接介面

### For Notebook PC: (accessory adapter)

- PCMCIA 2.0/2.1 and PC Card Standard compliant.

- Type II PC Card  3.37” x 2.128” x 0.197” (86mm x 54mm x 5.0mm)

- 50gw in weight with Compact Card

### For PDA/Palm PC: (Compact Card Only)

- CF+ and CompactFlash Spec. Rev. 1.4 compliant.

- Type I CompactFlash I/O Card 3.46” x 1.685” x 0.130” (88mm x 42.8mm x 3.3mm)

- 28gw in weight

電力需求

- 正常操作狀態: +3.3V, 50mA max

實體規格

- Type I CompactFlash I/O 介面

- 體積88mm x 42.8mm x 3.3mm

- 重量30gw

LED 指示燈

- Link (橘色:表正常連線)

- Act (綠色閃爍:表資料傳送中)

EMI 及 PTT 安規

- FCC part 15 Class B

- CE Mark EN55002 Class B, EN50081-2

外部環境需求

- 操作溫度：32(F to 149(F   (0(C to 65(C)

- 儲存溫度：-4(F to 158(F   (0(C to 70(C)

- 溼度：	10% - 90% , noncondensing